## Slide 1: Colocalization
Todd Fallesen

## Slide 2
Outline
2
  Colocalization
    What even is it
  Pixel Based
    Pearsons’s
    Spearman’s
    Manders
    Controls
  Object Based
    Basically, CellProfiler
  Reproducibility/Methods writing
Notes: Please feel free to ask questions

## Slide 3: What do we mean by Colocalization?
People mean different things by Colocalization.
    Do different markers show up in the same cell?
    Do objects overlap?
    Do proteins interact?
    Is a protein inside a cellular structure?

## Slide 4: Color Registration

## Slide 5: Pixel based Colocalization assessment is often visual
Simplest Case:
  Merge two fluorescence pseudo-colored images
  Assess whether different wavelengths are present in same pixels
    E.g. Red + Green = Yellow
  Problem:
    Intermediate color (e.g. yellow) only visible if probes overlap in similar proportions

## Slide 6: Color assessment doesn’t always work
Colors don’t always work. We can’t even see the white in some areas.

## Slide 7: Co-Occurance never actually happens!
Deconvolved Widefield
Confocal
Super-Resolution
There is no such thing as “colocalization”!

## Slide 8: what if DOTs overlap at max resolution?
Fluorophores reside within same volume.
Volume at least one order of magnitude larger than protein complexes

## Slide 9: Correlation is not causation
Colocalisation does not imply interaction
Non-colocalisation probably implies no interaction
Dividing line between colocalisation and non-colocalisation is arbitrary
Extent of colocalisation decreases with increasing spatial resolution
Chart: Spatial Resolution
| 1 | 2 | 3 | 4
Y-Values | 4 | 3 | 2 | 1
Demmerle et al., Nat Protocols, 2017
Relative Localisation
Correlation Analysis

## Slide 10
Two criteria must be met:
  Co-occurrence - spatial overlap of probes
  Correlation - probes are co-distributed
Distribution may overlap, but not proportionally
  DAPI will overlap with nuclear proteins, but will unlikely be proportional

## Slide 11: Intensity-based correlation coefficients
Pearsons
  Analysis of signal correlation
Spearmans
  Similar to Pearsons
  Less sensitive to outliers
Manders
  Analysis of signal overlap
Chart: Red

## Slide 12: Pearsons coefficient
Measures the linear correlation between two signals, looking at intensity levels of the two signals are on a pixel-by-pixel basis.
Range from -1 to 1, -1 is completely negatively correlated, +1 is correlated completely
Very sensitive of ROI placement. Imagine a single pixel, vs different ROI
Drawing an ROI is very difficult to automate, especially in 3D
Notes:   Kinesin on Microtubules would have a manders of 1, all kinesin is on microtubules, but not all microtubules are kinesin
  Microtuubule on kinesin channel would have a very low manders.

## Slide 13: Pearson’s correlation coefficient
Mean red intensity in whole image
Difference between each red pixel and the mean red intensity
Variance in red signal
The coefficient is normalised to the standard deviation across the two channels to ensure that values range from -1 to +1

## Slide 14: Pearson’s correlation coefficient
47.8 | 252.4
137.9 | 51.1
-74.5 | 130.1
15.6 | -71.2
Mean: 113.1
Mean: 122.3
113.3
122.3
-74.4 | X | -74.5 | = | 5543
74.4 | X | 130.1 | = | 9683
65.9 | X | 15.6 | = | 1026
-65.9 | X | -71.2 | = | 4690
5535 |  | 5550
4343 |  | 16926
4343 |  | 243
5535 |  | 5069
If two targets are functionally related, their abundances will be predictably related
 |  |  |  | 20944
19751 |  | 27788

## Slide 15: Noise results in “Less” correlation
Pcc = 0.41
Pcc = 0.33
Sample can exhibit high co-occurrence, but low correlation

## Slide 16: Filtering suppresses Noise
But information is lost!

## Slide 17: Pearson’s: Pros & Cons
Easy to measure
Broadly applicable
Independent of signal levels
Same amount of signal overlap can have dramatically different PCC values
Intermediate values difficult to interpret
Background pixels artificially inflate PCC values
Empty areas within cells have similar effect
Depends on linear relationship between probe intensities
PROS
CONS

## Slide 18: Spearman’s correlation coefficient
Pearson’s skewed by non-linearity, such as outliers
Spearman’s similar to Pearson’s, but compares ranks rather than values
Chart: 
| 238 | 114 | 9 | 7 | 500 | 23 | 18 | 147 | 14 | 1
 | 48 | 73 | 138 | 102 | 10000 | 186 | 169 | 11 | 82 | 37
Chart: 
| 2 | 4 | 8 | 9 | 1 | 5 | 6 | 3 | 7 | 10
 | 8 | 7 | 4 | 5 | 1 | 2 | 3 | 10 | 6 | 9
Red | Green | Rank Red | Rank Green
96 | 93 | 6 | 7
177 | 209 | 3 | 3
41 | 30 | 10 | 10
43 | 94 | 9 | 6
500 | 10000 | 1 | 1
112 | 165 | 4 | 4
102 | 234 | 5 | 2
194 | 75 | 2 | 8
79 | 104 | 7 | 5
64 | 52 | 8 | 9
Pc = 0.9
Sc = 0.1

## Slide 19
Both measure poorly the quantity that is typically at the heart of most analyses of colocalization in cell biology:
The fraction of one family of objects that localizes with another.

## Slide 20: Manders coefficient
Overlapping fraction method
Set a threshold for channel 1 and channel 2
The pixels stay the same value if above the threshold, 0 otherwise
Then calculate Manders coefficients M1 and M2
  M1 is the fraction of channel 1 that co-occurs with channel 2
  M2 is the fraction of channel 2 that co-occurs with channel 1
  Manders values are not equal between M1 and M2
  Manders doesn't equal volume overlap
Notes:   Kinesin on Microtubules would have a manders of 1, all kinesin is on microtubules, but not all microtubules are kinesin
  Microtuubule on kinesin channel would have a very low manders.

## Slide 21
Mred-green = 0.59
Mgreen-red = 0.68

## Slide 22: Mander’s coefficient
Independent of signal proportionality
Sensitive to co-occurrence, the fraction of pixels with signals from both channels
Overlap Coefficient:
Problem: Image must contain meaningful “zero” values.
Colocalisation Coefficient:

## Slide 23: Controls
Correlation coefficients mean little in isolation
  Analyses should include positive and negative controls
But, control samples may not exist
  Practical alternative: generate a “random” distribution by scrambling, translation or rotation.

## Slide 24: Generating controls
P = -0.06
P = 0.95
Original
Rotated 90°
Randomised
P = 0.00

## Slide 25: COLOC2 – FIJI Plugin for colocalisation analysis

## Slide 26: Object based Colocalization

## Slide 27: Overview
CellProfiler Operates on Objects
  Primary objects are easily segmentable objects we start with
  Secondary objects grow from Primary objects
  Tertiary objects are the subtraction of primary objects from secondary objects
  Objects are masks over any channel
  Almost all measurements are done on objects

## Slide 28: Usage tips
The easiest way to use CellProfiler is in GUI form, with all your images separated.
It is harder to work with image stacks, or hyperstacks.
  Separate z-stacks into image sequences
  Separate time-series out as well.
CellProfiler isn’t easy to use in 4D.

## Slide 29: Usage tips
The easiest way to use CellProfiler is in GUI form, with all your images separated.
It is harder to work with image stacks, or hyperstacks.
  Separate z-stacks into image sequences
  Separate time-series out as well.
CellProfiler isn’t easy to use in 4D.

## Slide 30: Loading Images
Drop files into the dialog box here

## Slide 31: Image Naming
Use rules to differentiate between images
Make sure that each channel has a unique identifier
Usually use the rules ‘Does’ or ‘Does not’ contain an expression. Avoid regular expressions.
Click update and make sure that everything is lined up properly
Numbering goes :
1,10,11,12,….19,2,20,21…….29,3,30…
Always number files 01,02, 03….10,11. etc.
If you will have more than a hundred images
001, 002, 003, ….010….099, 100;

## Slide 32: Objects
CellProfiler is a powerful segmentation tool. The result of segmentation are objects, which are the backbone of all subsequent processing.
  Objects can be extended to find secondary or tertiary objects
  Objects can be measured over multiple channels (i.e. use a nuclear object as a mask to measure the signal of another channel inside nuclei).
  Objects can be merged, split, eroded, filtered by measurements
  Objects can be tracked

## Slide 33: Primary Objects
Primary objects are those that are found from an image without any additional information.
Easily detectable objects, as opposed to confluent cells.
Can be found by image analysis techniques in CellProfiler
  Thresholding, watershed, etc.
Can be imported from outside image segmentation
  StarDist, Cellpose
IdentifyPrimaryObjects identifies biological objects of interest. It requires grayscale images containing bright objects on a dark background. Incoming images must be 2D (including 2D slices of 3D images); please use the Watershed module for identification of objects in 3D.

## Slide 34: Primary Objects
Primary objects are those that are found from an image without any additional information.
Easily detectable objects, as opposed to confluent cells.
Can be found by image analysis techniques in CellProfiler
  Thresholding, watershed, etc.
Can be imported from outside image segmentation
  StarDist, Cellpose
IdentifyPrimaryObjects identifies biological objects of interest. It requires grayscale images containing bright objects on a dark background. Incoming images must be 2D (including 2D slices of 3D images); please use the Watershed module for identification of objects in 3D.

## Slide 35: Thresholding
Global is more useful. If doing adaptive, then do illumination correction
Play with the thresholding method. The Otsu method lets you do a three class thresholding.
Declumping by intensity is useful if there is good demarcation between objects
Declumping by shape is useful if there is curvature between the objects

## Slide 36: Secondary Objects
Secondary objects use a primary object for reference in detection, i.e. a nuclei to start, and then propogate out to find cell boundary in cytoplasm
Tertiary objects are just secondary objects with the primary object removed (i.e. cytoplasm without the nuclei)

## Slide 37: Relating Objects
Relating objects gives a child-parent relationship between two sets of objects.
This would be for something akin to RNAScope, where you would want to count the number or intensity of labelled RNA inside a nucleus

## Slide 38: Relating Objects vs Secondary Objects
Secondary objects ‘grow’ from primary objects
Related objects are ‘inside’ other objects.
  The two related objects can both be primary objects.
  You can’t relate a secondary object set to the primary object set it grew from

## Slide 39: Object Measurements
You can measure a variety of parameters of the objects
  Intensity
    Total
    Gradients
  Colocalization
  Granularity
  Texture
  Size/Shape properties
    Area
    Eccentricity
  Number of Neighbors
You can plot within CellProfiler, but you can’t save the plots programmatically.

## Slide 40: Saving Data
Can export image files and csv files
Can also export databases for CellProfiler Analyst, which is beyond the scope of this class

## Slide 41: Task 4
Open the pipeline for Example Speckles and load the data
We’re going to explore this together

## Slide 42: StarDist (or CellPose)
StarDist is a plugin for FIJI that allows for quick segmentation of star-convex objects (round, nuclear shaped things).
StarDist can’t be run inside CellProfiler, but it’s a great trick to know
Running StarDist on a DAPI channel, and bringing those results in to CellProfiler as a separate image channel allows for easy nuclear segmentation
Stardist can only detect objects that are Star-convex: all the points of the perimeter can be reached by rays emanating from a point somewhere in the object.

## Slide 43: StarDist in FIJI
Need to add the CSBDeep and StarDist libraries
Run stardist on a nuclear image, and save the resulting prediction image as a tiff. The ‘pixel intensity’ of each nuclei is the nuclear ID label

## Slide 44: Macros Included
split_channel_multiple_series_and_rename.ijm – split images into single channel images
stardist_process_folder.ijm – run stardist on a specified channel in a folder of split images

## Slide 45: Documentation
Image analysis is like any other science experiment.
    Document what you do
    Document what experimental parameters you vary
    Record your steps!
    Make it reproducible
  FIJI Macro Recorder
  Write code from data to figure! Have it reproducible

## Slide 46: Extra help
https://www.ncbi.nlm.nih.gov/pmc/articles/PMC3074624/
https://imagej.net/imaging/colocalization-analysis